Fwrisc Pipelining
It is a five stage pipelined featherweight core. It is simulated by modelsim.
Main module is main_fw. Testbench is also present.
Design Modification:
- Data Memory interface
- PC Generation block
- Add pipes
- handling pipelining hazards
- Add flush and stall signals

Data Memory Interface
The Featherweight processor uses RAM of the FPGA for data and instruction memory. In order to simplify, data memory and instruction memory module has been added and interfaced with the main fwrisc design. Proper handshaking scheme has also been achieved.

PC Generation block
In the featherweight processor, the PC is updated in the execution phase. In order to pipeline it, the PC block has to be separated from the execution stage. So PC updation has been introduced in the fetch stage with the help of mux. The control signal of the mux, branch_taken, is coming from the execution stage which determines either the next PC should be PC plus four or the targeted address calculated at the execution stage.

Add pipes
After separating the PC block, pipes have been added. Four pipes are added aas
- Fetch to Decode stage
- Decode to Execution stage
- Execution to memory stage
- Memory to write-back stage

Handling pipeline hazards
There are three types of hazards faced while pipelining
- Structural Hazards
- Data Hazards
- Control hazards
Structural hazards are caused due to using the same hardware at different stages. As the PC generation block has already been separated from the execution stage and different memories are used for instructions and load/store, so in our design there is no structural hazard.

Data hazards occur when the operand of the current instruction is the destination of the previous instruction. In order to minimize this hazard, stalling and forwarding is used. In this design forwarding is used by comparing the operands of current instruction with the destination of previous instruction. If they match, then the output of the alu of the previous instruction is fed to the decoder of current instruction. For this two multiplexers and comparetors have been used. There will always be one stall for load instruction if data dependency occurs. It can not be removed. When dependency occurs, the decoder detects it and sends a stall signal to the fetch-decode pipe to wait one cycle which adds a stall.

Control hazards occur due to conditional jumps. It can be minimized by introducing branch predictors in the design. In this design branch prediction is not applied. Flushing is used to clear the data in pipes if branch is taken

Final modified design is: